## Slide 1
Gesture-Controlled Robotic Arm
Submitted By: Vishwas Patel
2427030557
Supervised By: Dr. Rishi Gupta
School of Computer Science and Engineering
Department of Computer Science and Engineering

## Slide 2
PROJECT OVERVIEW
What This Project Does
A robotic arm is controlled in real time using natural hand movements and gestures, captured through a standard webcam — no joystick, teach-pendant, or physical controller involved.
Hand pose and gestures are captured via webcam + computer vision
Recognized motion is converted into a target end-effector position
The robot (simulated MyCobot 280) follows the hand in real time
INPUT → OUTPUT
W
Webcam Feed
Live hand video input
G
Gesture Understanding
Position, depth estimate, pinch
R
Robot Motion (Simulated)
MyCobot 280 in RViz
2

## Slide 3
MOTIVATION
Why Gesture-Based Control?
TRADITIONAL CONTROL
Requires joysticks, teach pendants, or pre-programmed paths
Needs trained operators for setup and adjustment
Limited intuitiveness for quick or ad-hoc tasks
Physical controllers add cost and complexity
GESTURE-BASED CONTROL
Uses natural hand movement — no extra hardware controller
Faster, more intuitive interaction for simple tasks
Camera-based input is low-cost and easy to set up
Useful for education, prototyping, and assistive scenarios
3

## Slide 4
PROJECT OBJECTIVE
What We Set Out To Build
01
Real-Time Hand Tracking
Detect hand landmarks and gestures reliably from a live webcam feed.
02
Gesture-to-Motion Mapping
Convert hand position and gestures into a target robot end-effector position.
03
IK-Driven Robot Control
Use inverse kinematics to compute correct joint angles for that position.
04
Simulated Validation
Validate the complete pipeline on a MyCobot 280 in ROS 2 / RViz before hardware.
4

## Slide 5
SYSTEM ARCHITECTURE
End-to-End Pipeline
Webcam
OpenCV
MediaPipe
Hands
Hand Coords
+ Gesture
ROS 2
RViz /
MyCobot 280
Full detail: Webcam → OpenCV → MediaPipe Hands → Hand Landmarks → Palm Position + Depth + Gestures → Target Position → Inverse Kinematics → Joint Angles → ROS 2 → RViz → MyCobot 280
5
Target Pose /
Joint Angles (IK)

## Slide 6
TECHNOLOGY STACK
Tools & Frameworks In Use
Py
Python
Core language
CV
OpenCV
Webcam capture
MP
MediaPipe Hands
Landmark detection
R2
ROS 2 Jazzy
Robot middleware
Rv
RViz
3D visualization
Ux
URDF / Xacro
Robot model
IK
IKPy
Inverse kinematics
JS
sensor_msgs/
JointState
Joint communication
6

## Slide 7
PROGRESS ACHIEVED
What Has Been Implemented
✓
Webcam Input
Real-time capture using OpenCV
✓
Hand Tracking
MediaPipe Hands — 21 landmarks + palm center
✓
Hand Movement
X/Y from position, Z estimated from hand size
✓
Gesture Detection
Pinch gesture with hysteresis thresholds
✓
ROS 2 Communication
Joint states published on /joint_states (radians)
✓
Robot Simulation
MyCobot 280 integrated in ROS 2 / RViz, driven live by hand tracking
7

## Slide 8
INITIAL PROTOTYPE
Direct Mapping Approach
How the first working version worked:
Hand X / Y / Z
Selected Joint
Angles
Robot Moves
WHY IT WAS USEFUL
Proved the full pipeline end-to-end
Webcam → gestures → visible robot motion
Fast way to validate ROS 2 + RViz setup
KEY LIMITATION
Not genuine inverse kinematics
Joint angles were chosen directly from hand position, not computed from robot geometry
8

## Slide 9
CURRENT DEVELOPMENT
Moving To Inverse Kinematics
Desired End-
Effector Position
IK Solver
(IKPy)
Joint
Configuration
/joint_states
(ROS 2)
RViz
This replaces the earlier direct-mapping approach with joint angles computed from robot geometry.
IN PROGRESS
IKPy is being explored as the IK solver
Forward kinematics used to verify the resulting end-effector position
Position error is calculated between desired and achieved pose
KNOWN OPEN PROBLEMS
IK can yield multiple valid joint configurations
Solver joint names must correctly map to ROS joint names
9

## Slide 10
SMOOTHING & STABILITY
Handling Jitter and Signal Loss
Raw hand-tracking coordinates are noisy — smoothing keeps the robot's motion stable and natural.
1E
One Euro Filter
Being introduced to smooth hand-position signals
Aims to reduce jitter while keeping latency low
Applied before positions are sent to the IK stage
H
Hand-Loss Handling
If the hand temporarily leaves the camera view, the robot holds its last valid position
Prevents sudden, unintended arm motion from tracking dropouts
Both improvements target the same goal: keeping robot motion predictable and safe to watch during live control.
10

## Slide 11
CHALLENGES FACED
Real Obstacles Along the Way
Python / MediaPipe / NumPy version compatibility
ROS 2 and simulation environment setup
Understanding the MyCobot URDF structure
Mapping camera coordinates to robot coordinates
Hand-tracking jitter
Estimating depth from a normal (non-depth) webcam
IK yielding multiple possible joint configurations
Mapping IK solver joints to correct ROS joint names
Validating IK results using forward kinematics
11

## Slide 12
CURRENT PROJECT STATUS
At a Glance
Vision / hand tracking
WORKING
MediaPipe landmarks
WORKING
Gesture detection
WORKING
ROS 2 communication
WORKING
MyCobot 280 RViz simulation
WORKING
Basic hand-controlled simulation
WORKING
URDF-based inverse kinematics
IN PROGRESS
Smoothing / calibration
IN PROGRESS
Physical robotic arm
FUTURE WORK
12

## Slide 13
NEXT STEPS
Immediate Technical Goals
01
Finish IK Integration
Complete IKPy-based solving and connect it fully into the control loop.
02
Validate with Forward Kinematics
Cross-check IK output against desired position and quantify error.
03
Resolve Joint Name Mapping
Ensure IK solver joints map correctly to ROS 2 joint names.
04
Apply One Euro Filtering
Integrate smoothing into the live pipeline and tune parameters.
05
Improve Depth Estimation
Refine the hand-size-based Z estimation for more stable reach control.
06
Extended Testing in RViz
Stress-test the full pipeline across a wider range of hand motions.
13

## Slide 14
LIVE DEMONSTRATION
What you'll see next, running live:
1
MediaPipe hand tracking on live webcam feed
2
Hand movement driving robot target position
3
Pinch gesture recognition
4
ROS 2 /joint_states being published
5
MyCobot 280 motion in RViz
14